Device Interfacing
with Python and ZIO
vijaykumar@zilogic.com
Zilogic Systems

---
Overview
ZIO Architecture
ZIO Ports
LED
Switch
Light Sensor
DC Motor
Temp Sensor
TV Remote Receiver
Color Sensor
Light Bulb

---
ZIO Architecture
Sensors
Transistors
Relays
LEDs
Switches
I2C Devices
DC Motors
IR receivers
...
USB based IO board
Digital I/O
Analog Input
PWM Output
I2C Bus
SPI Bus
PC – The Universal Platform
API to communicate with ZIO

---
Ports
GPIO
  - LEDs, Relays, Switches, MOSFETs, Optocouplers, ...
Sensor
  - Tempature, Potentiometer, Light, Pressure, Humidity, ...
PWM
  - DC Motor, Servo Motor, LED Brightness Control, ...
I2C/SPI
  - RTCs, LCDs, IR Receivers, Sensors, Phone Line Interface ...

---
LED
Simple output devices
Used for status indication, displays, lighting ...

---
LED (Contd.)

---
Interface LED to ZIO
GPIO Port
Signals
  - 2 Outputs, 2 Inputs
  - +5V Supply, GND
Setting Output to True, outputs 0V
Setting Output to False, outputs 5V

---
Interface LED to ZIO (Contd.)
GPIO outputs have a built-in series resistor
Eliminates series resistors on external circuit

---
Interface LED to ZIO (Contd.)
from zio import *
agent = Agent(“/dev/ttyUSB0”)
gpio = GPIO(agent)
gpio.write_output_pin(0, True)
gpio.write_output_pin(0, False)

---
Voltage Divider

---
Switch
Simple input device
Switch is closed
  - Vout = 0V
Switch is open
  - Vout = 5V
Switch state can be determined, by measuring Vout.

---
Interface Switch to ZIO
GPIO Input signals can test for a 0V or 5V.
Input > 2V
  - Read as True
Input < 0.8V
  - Read as False

---
Interface Switch to ZIO (Contd.)
GPIO inputs have built-in pull-ups resistors
Eliminates pull-ups on external circuits

---
Interface Switch to ZIO (Contd.)
import time
from zio import *
agent = Agent(“/dev/ttyUSB0”)
gpio = GPIO(agent)
while True:
  - print gpio.read_input_pin(0)
  - time.sleep(1)

---
Light Sensor (LDR)
LDR – Light Dependent Resistor
Resistance decreases with increase in light intensity
Voltage Vout decreases with increase in light intensity

---
Interface LDR to ZIO
Sensor port
  - measure voltages between 0 – 3V
Signals
  - +5V, GND
  - 2 Sensor Inputs
Read the voltage at Sensor 0

---
Interface LDR to ZIO (Contd.)
Sensor inputs have built-in pull-up resistors
Eliminates pull-ups on external circuits
Pull-ups connected to 3V, the max voltage that can be measured by sensor port.

---
Interface LDR to ZIO (Contd.)
import time
from zio import *
agent = Agent(“/dev/ttyUSB0”)
sensor = Sensor(agent)
while True:
  - print sensor.read_pin(0)
  - time.sleep(1)

---
DC Motor
Examples
  - CPU Fan
  - Wheels of a Robot
  - CDROM drives
  - Printers
DC motor controlled by a human operated switch

---
DC Motor (Contd.)
Replace switch by a MOSFET
Vcontrol = 5V
  - Motor turns ON
Vcontrol = 0V
  - Motor turns OFF

---
DC Motor (Contd.)
GPIO port - motor ON and OFF
Motor speed can be controlled
DC motor speed is propotional to the supply voltage
Speed control can be acheived by varying the averaging voltage delivered to the motor

---
DC Motor (Contd.)
Rapidly turn motor on and off
Duty cycle
  - (ON time / Period) * 100
Duty cycle 100%
  - Average voltage - 12V
Duty cycle 50%
  - Average voltage - 6V

---
Interface DC Motor to ZIO
pwm = PWM(agent)
pwm.set_freq([0], 25)
pwm.set_duty([0], 100)
pwm.start([0])
pwm.set_duty([0], 50)
pwm.set_duty([0], 25)

---
Temperature Sensor
Temperature Sensors
  - Resistive Sensors
  - Non-ratiometric Sensors
  - I2C / SPI Sensors
I2C
  - kind of very simplified USB
  - connect devices to CPU
  - EEPROMs, RTCs, Accelerometers, Sensors ...

---
I2C Bus

---
Temperature Sensor
i2c = I2C(agent)
i2c.config(100)
while True:
  - temp = i2c.read(0x10, 1)
  - print temp[0]

---
Demo Projects
TV Remote Receiver
Light Bulb
Color Sensor